## Slide 1: Fetch decode execute cycle
Fetch :
Get an instruction from main memory
Decode:
Translate it into computer command
Execute:
Actual processing of command
Store/Write back:
Write result to memory.

## Slide 2: Fetch decode execute cycle

## Slide 3: The Fetch/Execute Cycle
“Instruction Execution Engine”…a machine that cycles through a series of operations
Series is called: Fetch/Execute Cycle
  Get the next instruction
  Figure out what to do
  Gathering the data needed to do it
  Do it
  Save the result, and
  Repeat (billions of times/second)!

## Slide 4: A Five-Step Cycle
These operations are repeated in a never-ending sequence
A five-step cycle:
  Instruction Fetch (IF)
  Instruction Decode (ID)
  Data Fetch (DF) / Operand Fetch (OF)
  Instruction Execution (EX)
  Result Return (RR) / Store (ST)

## Slide 5: A Five-Step Cycle

## Slide 6: ADD 800, 428, 884

## Slide 7: Instruction Fetch (IF)
Execution begins by moving the instruction at the address given by the (PC 2200) from memory to the control unit
Once instruction is fetched, the PC can be changed for fetching the next instruction

## Slide 8: IF
Notes: Execution begins by moving the instruction at the address given by the PC (PC 2200) from memory to the control unit
Once instruction is fetched, the PC can be readied for fetching the next instruction

## Slide 9: Instruction Decode (ID)
ALU is set up for the operation
Decoder finds the memory address of the instruction's data (source operands)
  Most instructions operate on two data values stored in memory (like ADD), so most instructions have addresses for two source operands
  These addresses are passed to the circuit that fetches them from memory during the next step
  Decoder finds the destination address for the Result Return step and places the address in the RR circuit
  Decoder determines what operation the ALU will perform (ADD), and sets up the ALU

## Slide 10: ID

## Slide 11: Data Fetch (DF)
The data values to be operated on are retrieved from memory
Bits at specified memory locations are copied into locations in the ALU circuitry
Data values remain in memory (they are not destroyed)

## Slide 12: DF

## Slide 13: Instruction Execution (EX)
For this ADD instruction, the addition circuit adds the two source operands together to produce their sum
Sum is held in the ALU circuitry
This is the actual computation

## Slide 14: EX

## Slide 15: Return Result (RR)
RR returns the result of EX to the memory location specified by the destination address.
Once the result is stored, the cycle begins again

## Slide 16: RR

## Slide 17: Cycling the Fetch/Execute Cycle
ADD is representative of the complexity of computer instructions…some are slightly simpler, some slightly more complex
Computers achieve success at what they can do with speed.
They show their impressive capabilities by executing many simple instructions per second

## Slide 18: Many, Many Simple Operations
Computers “know” very few instructions
The decoder hardware in the controller recognizes, and the ALU performs, only about 100 different instructions (with a lot of duplication)
There are only about 20 different kinds of operations.
Everything that computers do must be reduced to some combination of these primitive, hardwired instructions

## Slide 19: Processor and Memory

## Slide 20: Memory
Memory stores both the program while it is running and the data on which the program operates
Properties of memory:
  Discrete locations
    Memory is organized as a sequence of discrete locations
    In modern memory, each location is composed of 1 byte (8 bits)

## Slide 21: Memory
Addresses
  Every memory location has an address, whole numbers starting at 0
Values
  Memory locations record or store values
Finite capacity
  Memory locations have a finite capacity (limited size),
  Data may not “fit” in the memory location

## Slide 22: Byte-Size Memory Location
Common visualization of computer memory
Discrete locations are shown as boxes holding 1-byte each
Address of location is displayed above the box and the contents of location is shown in the box

## Slide 23: Byte-Size Memory Location
That 1-byte memory location can store one ASCII character or a number less than 256
Blocks of four bytes are used as a unit so often that they are called memory words.

## Slide 24: RAM
Computer memory is called random access memory (RAM)
  “Random access” is out-of-date and simply means that the computer can refer to the memory locations in any order
RAM is measured in megabytes (MB) or gigabytes (GB)
Lots of memory is need to handle the space required of programs and data

## Slide 25: Storage Evaluation Criteria
Property | Desirable | Primary storage | Secondary storage
Storage capacity | Large storage capacity | Small | Large
Access Time | Fast access time | Fast | Slow
Cost per bit of storage | Lower cost per bit | High | Low
Volatility | Non-volatile | Volatile | Non-volatile
Access | Random access | Random access | Pseudo-random access or sequential access

## Slide 26: Memory Capacity
Memory capacity of a computer is equal to the number of bytes that can be stored in its primary storage
Its units are:
Kilobytes (KB) : 1024 (210) bytes
Megabytes (MB) : 1,048,576 (220) bytes
Gigabytes (GB) : 1,073,741824 (230) bytes

## Slide 27: Control unit-CU
The control unit of a computer is where the Fetch/Execute Cycle occurs
Its circuitry fetches an instruction from memory and performs the other operations of the Fetch/Execute Cycle on it
A typical machine instruction has the form ADD 4000, 2000, 2080

## Slide 28: Task
ADD 4000, 2000, 2080
  Looks like those three numbers should be added together
  What it really means is that whatever numbers are stored in memory locations 2000 and 2080 be added together, and the result be stored in location 4000

## Slide 29: task

## Slide 30: Storage Hierarchy
Capacity and access are inversely proportional to each other

## Slide 31: The Program Counter (PC)
How does the computer determine which instruction it should execute next?
Address of the Next Instruction
  The instruction is stored in memory and the computer has its address
  Computers use the address (known as the program counter or PC) to keep track of the next instruction

## Slide 32: The Computer Clock
Computers are instruction execution engines.
Since the computer does one instruction per cycle in principle, the speed of a computer depends on the number of Fetch/Execute Cycles it completes per second.

## Slide 33: The Computer Clock
The rate of the Fetch/Execute Cycle is determined by the computer’s clock, and it is measured in megahertz, or millions (mega) of cycles per second (hertz).
A 1,000 MHz clock ticks a billion (in American English) times per second, which is one gigahertz (1 GHz)

## Slide 34: Standard Prefixes

## Slide 35: One Cycle per Clock Tick
A computer with a 1 GHz clock has one billionth of a second—one nanosecond—between clock ticks to run the Fetch/Execute Cycle.
In that amount of time, light travels about one foot (~30 cm).
Modern computers try to start an instruction on each clock tick.

## Slide 36: Computer’s View of Software
Once installed, the computer runs the software by:
  copying the binary instructions into the RAM
  interpreting them using the Fetch/Execute Cycle.
It does whatever the instructions tell it to do

## Slide 37: Processor Speed
Computer has a built-in system clock that emits millions of regularly spaced electric pulses per second (known as clock cycles)
It takes one cycle to perform a basic operation, such as moving a byte of data from one memory location to another
Normally, several clock cycles are required to fetch, decode, and execute a single program instruction
Hence, shorter the clock cycle, faster the processor
Clock speed (number of clock cycles per second) is measured in Megahertz (106 cycles/sec) or Gigahertz (109 cycles/sec)